## Slide 1: Architecture Exploration of Standard-Cell and FPGA-Overlay CGRAs Using the Open-Source CGRA-ME Framework
S. Alexander Chin, Kuang Ping Niu, Matthew Walker, Shizhang Lin, Alexander Mertens, Jongeun Lee, Jason H. Anderson
ACM ISPD, Seaside, CA
March 26, 2018

## Slide 2: What are Coarse-Grained Reconfigurable Arrays (CGRAs)?
A style of programmable logic device between an ASIC and an FPGA on the programmability spectrum
Large coarse-grained blocks, datapath interconnect
  Blocks may be entire ALUs
  Interconnect 16/32-bit wide
Tailor CGRA block functionality to application domain:
  DSP
  Machine learning
  Finance
  …

## Slide 3: Example CGRA Architectures (1)
RaPiD / Totem Project
PipeRench

## Slide 4: Example CGRA Architectures (2)
ADRES

## Slide 5: Multiple Contexts
FPGAs have a static configuration: configure then use
Some CGRAs are “multi-context”:
  Multiple configurations are stored in the CGRA
  Each configuration is called a context
  Rotate through configurations on a cycle-by-cycle basis
    Logic functionality and routing paths change
+
X
>>
OR
/
AND
Context 0
Context 1

## Slide 6: Example CGRA Architectures (3)
SRP (Samsung)
DRP (Renesas / NEC)

## Slide 7: Efficiency vs. Programmability
Programmability
Efficiency
Custom ASIC
CGRA
GPGPU
General Purpose
Processor
FPGA
Typical application:
FPGA 300 MHz, 10 W
ASIC 1.2 GHz, 2.5 W
CGRA 1 GHz, 3 W
Must “stitch together” many LUTs, interconnect segments to implement functionality on FPGA
Large coarse-grained blocks aligned to application, bus-based routing
Notes: highlight the different types of CGRAs
commonality is that dataflow is paramount
efficiency stems from spatial computing at the instruction level
*** For domain specific computing
TODO: GPGPU picture, CPU picture

## Slide 8: Efficiency vs. Programmability
Programmability
Efficiency
Custom ASIC
CGRA
GPGPU
General Purpose
Processor
FPGA
FPGA Overlay
Notes: highlight the different types of CGRAs
commonality is that dataflow is paramount
efficiency stems from spatial computing at the instruction level
*** For domain specific computing
TODO: GPGPU picture, CPU picture

## Slide 9: FPGA Overlays
Overlays are a layer of abstraction on top of FPGAs
Pre-compiled architectures that are further programmable
  e.g. soft-processors, stream processors, coarse-grained reconfigurable arrays – FPGA Overlay CGRA
Benefits of overlays:
  Ease of use – compile software to configure the overlay
  Can be optimized towards specific application domains

## Slide 10: Overlays / FPGA Ease-of-Use
Two main challenges with FPGA ease-of-use:
1) Require HW design expertise
2) Lengthy compile times: hours/days
HLS addresses #1
Overlays aim to address both

## Slide 11: Vision: Overlays / FPGAs in the Cloud
Envision a library of FPGA accelerator overlays in cloud
Choose the overlay that best meets application’s needs
Map software application onto overlay accelerator
computational
finance
Application to accelerate
Library of pre-compiled cloud-deployed FPGA-Overlay CGRA accelerators

## Slide 12: CGRA Challenges
Architectures less studied than competition, such as FPGAs or GPGPUs
CAD tool development required
FPGAs:
Verilog-to-Routing
GPUs:
GPGPU-Sim
CGRAs: ???
Notes: - why cgra

## Slide 13: Introduction to CGRA-ME
CGRA-ME is an open-source modelling and exploration framework for CGRA architecture and CAD exploration
Project objectives:
  Allow an architect to model a wide range of CGRA architectures through an XML-based language
  Allow an application, described in a high-level language, to be mapped onto the modelled CGRA
  Simulation and verification of application on modelled CGRA
  Physical realization of the CGRA as an ASIC or FPGA overlay
  High-level area, performance, and power modelling of the CGRA for an application

## Slide 14
CGRA-ME: Framework Overview
Notes: Xander starts here

## Slide 15: CGRA-ADL (1)
XML-based description language for architects
  Describe CGRA blocks, their layout and hierarchy
  Describe interconnect within the CGRA
I/O
I/O
B0
B1
B(X)
B(X+1)
I/O
I/O
…
…

## Slide 16: CGRA-ADL (2)

## Slide 17: CGRA-ADL (3)

## Slide 18: CGRA-ADL (4)
Language has constructs to model CGRA at top-level
  Homogeneous or heterogeneous

## Slide 19
CGRA-ME: Framework Overview
Notes: Xander starts here

## Slide 20: Mapping Applications to a CGRA
Front-end data-flow graph extraction - LLVM
  State-of-the-art compiler used by Apple, NVIDIA, Xilinx, Intel, etc
  Leverage LLVM language support, parsing and optimizations
In LLVM, the program is represented in an Intermediate Representation (IR)
  Machine-independent assembly code
  Limited instruction set: add, xor, branch, mul, div
Target inner-loop kernels for mapping to CGRAs

## Slide 21: Data-Flow Graph Extraction
FFT IR code in LLVM

## Slide 22: LLVM IR-based CGRA Functional Units
We align the functionality specification of CGRA blocks with the LLVM IR computational instructions
The capabilities of the architecture are expressed in the same instruction set as the compiler to the architecture
FU
REG
Example Block
mul | add | mul->add

## Slide 23
CGRA-ME: Framework Overview
Notes: Xander starts here

## Slide 24: Mapping Background
Three main tasks
Scheduling
  determine when to perform an operation
Placement
  determine which functional unit should perform an operation
Routing
  Ensure a valid route for value between subsequent operations
Modulo Routing Resource Graph

## Slide 25: Modulo Routing Resource Graph
FU
REG
Example Block
Generalizable – handles multiple configuration contexts
Piecemeal construction
From previous clock cycle
To next clock cycle

## Slide 26: 2-context Example
Data Flow Graph
Cycle / Context 0
Cycle / Context 1
Two Mappers:
Simulated annealing
Integer Linear Programming (DAC 2018)

## Slide 27: CGRA Mapping Using Integer Linear Programming
Consider mapping problem as a constraint problem - ILP
Formulation “highlights”:
  Consider two sets of binary variables
  Fp,q if 1, Op q is mapped to FU p
  Ri,j if 1, Val j is mapped to RR i
Every Op must be mapped to a Functional Unit:

## Slide 28: Mapping Algorithm: Integer Linear Programming (cont’d)
At most one Op can be mapped to a Functional Unit
Values cannot use the same routing resource
Additional constraints guarantee that values are routed from Op outputs to Op inputs.

## Slide 29
CGRA-ME: Framework Overview
Notes: Xander starts here

## Slide 30
Verilog Generation (1)
Generate RTL for:
  Simulation / Verification
  Std. cell Synthesis
  FPGA-overlay Synthesis

## Slide 31: Verilog Generation (2)
Func. U.
C
io
io
Func. U.
C
ALU
ALU
Func. U.
C
C
ALU
ALU
CGRA
Take the module tree that the MRRG was generated from, and emit a parameterized Verilog file for each module type:
  Includes ports, sub-module declarations, and a generic implementation of the block.
Modules for configuration are also added to the parent module of their configuration target
  Automatically connected to the right module, and linked together to form an inter-module scan chain.
FU
IO
IO
IO
FU
FU
FU
FU
FU
FU
FU
FU

## Slide 32: Configuration Bitstream Generation
FU
REG
+
DFG
MRRG
Modules
A successful mapping associates all nodes and edges in the DFG with one or more MRRG nodes.
Iterate the configuration sub-modules, generate a configuration bitstream for the submodule for the application.

## Slide 33: Functional Verification
Configuration bitstream is emitted as part of a “configurator” Verilog module
Testbench instantiates configurator & CGRA, provides clock signal, etc.
Permits functional verification of the CGRA as configured for an application
Testbench
configurator.v
CGRA.v
CGRA-ME
ModelSim
Configuration Gen.
Verilog Gen.
benchmark.c

## Slide 34: Experimental Study (1)
We compare two variations of 4x4 ADRES:
  Homogeneous with torus connections
    every PE can do full set of ops (mul, shift, add/sub, logical)
  Heterogeneous without torus connections
    every other columns’ PEs can do reduced set of ops (add/sub)

## Slide 35: Experimental Study (2)
Verilog implementations are generated by the framework, and are synthesized for:
  Standard-cell Implementation: FreePDK45 standard-cell library
  FPGA-overlay Implementation: Stratix IV
10 benchmarks mapped to both architectures

## Slide 36: ILP Mapping Results

## Slide 37: Standard Cell CGRA
Targeting FreePDK45 standard cell library
  Open source 45nm standard cell library
  Implementation is not optimal, but allows relative comparisons between architectures
Synthesized with Synopsys Design Compiler
Place and route with Cadence Innovus (floorplanned)
STA performed using Synopsys Prime Time
Two targeted objectives
  Minimal delay
  Minimal area

## Slide 38: Standard Cell CGRA
Generic floorplan for ADRES-like architectures:

## Slide 39: Standard Cell CGRA

## Slide 40: Standard Cell CGRA
Comparison between architectures and objectives:

## Slide 41: Standard Cell CGRA

## Slide 42: FPGA-Overlay CGRA (1)
Implemented same architectures on Stratix IV (45nm Altera/Intel FPGA)
  Exactly same CGRA Verilog specification as in the standard-cell case
Floorplanned to ensure physical tile ordering in layout matches with “expected” ordering (e.g. col 2 tiles are to the right of col 1 tiles, etc)
Challenge:
  DSP tiles in Stratix IV are organized into columns
  Columns of DSPs are far apart -- considerably more LUT-based logic between DSP columns than needed
  Result: somewhat “loose” layout

## Slide 43: FPGA-Overlay CGRA (2)
Full
Reduced

## Slide 44: Current and Future Work
Compact area, delay and power models
  Create models for the frequently occurring CGRA components: MUXes, register file, config, functional units.
  Permit quick estimates of CGRA power, performance, area, without a full standard-cell or FPGA-overlay synthesis
Improving standard-cell and FPGA overlay physical realizations
Multiple context support
Integration with a processor simulator such as Gem5

## Slide 45: Summary
Standard-cell coarse-grained reconfigurable arrays (CGRAs) aim to provide (some of) the programmability of FPGAs with the speed/area/power of custom ASICs
FPGA-overlay CGRAs aim to provide faster programmability with software speed compile times
Many CGRAs proposed in academia/industry
  No framework to scientifically evaluate/compare
CGRA-ME provides a platform for CGRA architecture and CAD research

## Slide 46
Follow the Project: http://cgra-me.ece.utoronto.ca